## Slide 1: Digital Logic & Systems Shift Registers
Wenye Li, Ph.D
The Chinese University of Hong Kong

## Slide 2
A shift register is an arrangement of flip-flops with important applications in storage and movement of data. Some basic data movements are illustrated here.
Summary
Basic Shift Register Operations
Data in
Data in
Data in
Data in
Data in
Data out
Data out
Data out
Data out
Data out
Serial in/shift right/serial out
Serial in/shift left/serial out
Parallel in/serial out
Parallel in/parallel out
Serial in/parallel out
Rotate right
Rotate left

## Slide 3
Summary
Serial-in/Serial out Shift Register
Shift registers are available in IC form or can be constructed from discrete flip-flops as is shown here with a five-bit serial-in serial-out register.
Each clock pulse will move an input bit to the next flip-flop. For example, a 1 is shown as it moves across.
1
1
1
1
1
1
CLK
CLK
CLK
CLK
CLK

## Slide 4
Summary
A Basic Application
An application of shift registers is conversion of serial data to parallel form.
For example, assume the binary number 1011 is loaded sequentially, one bit at each clock pulse.
CLK
CLK
CLK
CLK
After 4 clock pulses, the data is available at the parallel output.

## Slide 5
Summary
The 74HC164A Shift Register
The 74HC164A is a CMOS 8-bit serial in/parallel out shift register. VCC can be from +2.0 V to +6.0 V.
One of the two serial data inputs may be used as an active HIGH enable to gate the other input. If no enable is needed, the other serial input can be connected to VCC. The 74HC164A has an active LOW asynchronous clear. Data is entered on the leading-edge of the clock.
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B

## Slide 6
Summary
Waveforms for the 74HC164A
Sample waveforms for the 74HC164A are shown. Notice that B acts as an active HIGH enable for the data on A as discussed.
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B
Outputs
Clear
Clear
As with CMOS devices, unused inputs should always be connected to a logic level; unused outputs should be left open.

## Slide 7
Summary
Parallel in/Serial out Shift Register
Shift registers can be used to convert parallel data to serial form. A logic diagram for this type of register is shown:
D0
D1
D2
D3
Q0
Q1
Q2
Q3
SHIFT/LOAD
CLK
Serial data out

## Slide 8
Summary
The 74HC165 Shift Register
The 74HC165 is a CMOS 8-bit parallel in/serial out shift register. The logic symbol is shown:
D0
D1
D2
D3
D4
D5
D6
D7
Q7
Q7
SH/LD
CLK
SER
CLK INH
The clock (CLK) and clock inhibit (CLK INH) lines are connected to a common OR gate, so either of these inputs can be used as an active-LOW clock enable with the other as the clock input. Data is loaded asynchronously when SH/LD is LOW and moved through the register synchronously when SH/LD is HIGH and a rising clock pulse occurs.

## Slide 9
Summary
Bidirectional Shift Register
Bidirectional shift registers can shift the data in either direction using a RIGHT/LEFT input.

## Slide 10
Summary
Bidirectional Shift Register
CLK
RIGHT/LEFT
Serial data in
Q0
Q1
Q2
Q3
Shift right
Shift left
Question
How will the pattern change if the RIGHT/LEFT control signal is inverted?
Answer
See display
Shift right
Shift left

## Slide 11
Summary
Universal Shift Register
A universal shift register has both serial and parallel input and output capability. The 74HC194 is an example of a 4-bit bidirectional universal shift register.
D0
D1
D2
D3
CLK
SL SER
Q0
Q1
Q2
Q3
SR SER
S1
S0
CLR
Sample waveforms are on the following slide…

## Slide 12
Summary
Universal Shift Register

## Slide 13
Summary
Shift Register Counters
Shift registers can form useful counters by recirculating a pattern of 0’s and 1’s. Two important shift register counters are the Johnson counter and the ring counter.
The Johnson counter can be made with a series of D flip-flops
… or with a series of J-K flip flops. Here Q3 and Q3 are fed back to the J and K inputs with a “twist”.

## Slide 14
Summary
Johnson Counter
“twist”
Redrawing the same Johnson counter (without the clock shown) illustrates why it is sometimes called as a “twisted-ring” counter.

## Slide 15
Summary
Johnson Counter
The Johnson counter is useful when you need a sequence that changes by only one bit at a time but it has a limited number of states (2n, where n = number of stages).
The first five counts for a 4-bit Johnson counter that is initially cleared are: CLK Q0 Q1 Q2 Q3
0 0 0 0
1 0 0 0
1 1 0 0
1 1 1 0
1 1 1 1
0 1 1 1
0 0 1 1
0 0 0 1
0
1
2
3
4
5
6
7
What are the remaining 3 states?
Question

## Slide 16
Summary
Ring Counter
The ring counter can also be implemented with either D flip-flops or J-K flip-flops.
Here is a 4-bit ring counter constructed from a series of D flip-flops. Notice the feedback.
Like the Johnson counter, it can also be implemented with J-K flip flops.

## Slide 17
Summary
Ring Counter
Redrawing the Ring counter (without the clock shown) shows why it is a “ring”.
The disadvantage to this counter is that it must be preloaded with the desired pattern (usually a single 0 or 1) and it has even fewer states than a Johnson counter (n, where n = number of flip-flops.
On the other hand, it has the advantage of being self-decoding with a unique output for each state.

## Slide 18
Summary
Ring Counter
A common pattern for a ring counter is to load it with a single 1 or a single 0. The waveforms shown here are for an 8-bit ring counter with a single 1.

## Slide 19
Summary
Shift Register Applications
Shift registers can be used to delay a digital signal by a predetermined amount.
Example
An 8-bit serial in/serial out shift register has a 40 MHz clock. What is the total delay through the register?
Solution
The delay for each clock is 1/40 MHz = 25 ns
The total delay is 8 x 25 ns = 200 ns
25 ns
= 200 ns

## Slide 20
Key Terms
Register
Stage
Shift
Load
Bidirectional
One or more flip-flops used to store and shift data.
One storage element in a register.
To move binary data from stage to stage within a shift register or other storage device or to move binary data into or out of the device.
To enter data in a shift register.
Having two directions. In a bidirectional shift register, the stored data can be shifted right or left.

## Slide 21
1. The shift register that would be used to delay serial data by
4 clock periods is
a. c.
b. d.
Quiz

## Slide 22
Quiz
2. The circuit shown is a
a. serial-in/serial-out shift register
b. serial-in/parallel-out shift register
c. parallel-in/serial-out shift register
d. parallel-in/parallel-out shift register

## Slide 23
Quiz
3. If the SHIFT/LOAD line is HIGH, data
a. is loaded from D0, D1, D2 and D3 immediately
b. is loaded from D0, D1, D2 and D3 on the next CLK
c. shifted from left to right on the next CLK
d. shifted from right to left on the next CLK

## Slide 24
Quiz
4. A 4-bit parallel-in/parallel-out shift register will store data for
a. 1 clock period
b. 2 clock periods
c. 3 clock periods
d. 4 clock periods

## Slide 25
5. The 74HC164 (shown) has two serial inputs. If data is placed on the A input, the B input
a. could serve as an active LOW enable
b. could serve as an active HIGH enable
c. should be connected to ground
d. should be left open
Quiz
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B

## Slide 26
Quiz
6. An advantage of a ring counter over a Johnson counter is that the ring counter
a. has more possible states for a given number of flip-flops
b. is cleared after each cycle
c. allows only one bit to change at a time
d. is self-decoding

## Slide 27
Quiz
7. A possible sequence for a 4-bit ring counter is
a. … 1111, 1110, 1101 …
b. … 0000, 0001, 0010 …
c. … 0001, 0011, 0111 …
d. … 1000, 0100, 0010 …

## Slide 28
Quiz
8. The circuit shown is a
a. serial-in/parallel-out shift register
b. serial-in/serial-out shift register
c. ring counter
d. Johnson counter

## Slide 29
9. Assume serial data is applied to the 8-bit shift register
shown. The clock frequency is 20 MHz. The first data bit
will show up at the output in
a. 50 ns
b. 200 ns
c. 400 ns
d. 800 ns
Quiz

## Slide 30
Answers:
1. a
2. c
3. c
4. a
5. b
6. d
7. d
8. d
9. c
Quiz