## Slide 1: Digital Logic & Systems Data Storage
Wenye Li, Ph.D
The Chinese University of Hong Kong

## Slide 2
Memories store data in units from one to eight bits. The most common unit is the byte, which by definition is 8 bits.
Summary
Memory Units
Computer memories are organized into multiples of bytes called words. Generally, a word is defined as the number of bits handled as one entity by a computer. By this definition, a word is equal to the internal register size (usually 16, 32, or 64 bits).
For historical reasons, assembly language defines a word as exactly two bytes. In assembly language, a 32 bit entity is called a double-word and 64 bits is defined as a quad-word.

## Slide 3
The location of a unit of data in a memory is called the address. In PCs, a byte is the smallest unit of data that can be accessed.
Summary
Memory Units
In a 2-dimensional array, a byte is accessed by supplying a row number. For example the blue byte is located in row 7.

## Slide 4
A 3-dimensional array is arranged as rows and columns. Each byte has a unique row and column address.
Summary
Memory Addressing
Question
How many bytes are shown?
What is the location of the blue byte?
Answers
b) Row 2, column 8
This example is (of course) only for illustration. Typical computer memories have 256 MB or more of capacity.
a) 64 B

## Slide 5
In order to read or write to a specific memory location, a binary code is placed on the address bus. Internal decoders decode the address to determine the specific location. Data is then moved to or from the data bus.
Summary
Memory Addressing
The address bus is a group of conductors with a common function. Its size determines the number of locations that can be accessed. A 32 bit address bus can access 232 locations, which is approximately 4G.

## Slide 6
Summary
Memory Addressing
In addition to the address bus and data bus, semiconductor memories have read and write control signals and chip select signals. Depending on the type of memory, other signals may be required.
Chip Select (CS) or Chip Enable (CE) is used as part of address decoding. All other inputs are ignored if the Chip Select is not active.
Read Enable (RE) and Write Enable (WE) signals are sent from the CPU to memory to control data transfer to or from memory.
Output Enable (OE) is active during a read operation, otherwise it is inactive. It connects the memory to the data bus.

## Slide 7
Summary
Read and Write Operations
The two main memory operations are called read and write. A simplified write operation is shown in which new data overwrites the original data. Data moves to the memory.
The address is placed on the address bus.
Data is placed on the data bus.
A write command is issued.
Address register
Data register
Address bus
Address decoder
Byte organized memory array
Write
Data bus

## Slide 8
Summary
Read and Write Operations
The read operation is actually a “copy” operation, as the original data is not changed. The data bus is a “two-way” path; data moves from the memory during a read operation.
The address is placed on the address bus.
A read command is issued.
A copy of the data is placed in the data bus and shifted into the data register.
Address register
Data register
Address bus
Address decoder
Byte organized memory array
Read
Data bus

## Slide 9
RAM is for temporary data storage. It is read/write memory and can store data only when power is applied, hence it is volatile. Two categories are static RAM (SRAM) and dynamic RAM (DRAM).
Summary
Random Access Memory
Bits stored in a semiconductor latch or flip-flop
Bits stored as charge on a capacitor

## Slide 10
SRAM uses semiconductor latch memory cells. The cells are organized into an array of rows and columns.
Summary
Static RAM
SRAM is faster than DRAM but is more complex, takes up more space, and is more expensive. SRAMs are available in many configurations – a typical large SRAM is organized as 512 k X 8 bits.

## Slide 11
Summary
Asynchronous Static RAM
The basic organization of an asynchronous SRAM is shown.
Read cycle sequence:
A valid address is put on the address bus
Chip select is LOW
Output enable is LOW
Data is placed on the data bus
Write cycle sequence:
A valid address is put on the address bus
Chip select is LOW
Write enable is LOW
Data is placed on the data bus
Address lines
Address lines
Eight
input buffers
I/O0
I/O7
Output data
CS
OE
WE
Row
decoder
Memory array
Column I/O
Column decoder
256 rows x
128 columns x
8 bits
Input data control

## Slide 12
Summary
Dynamic RAM (DRAM)
Dynamic RAMs (DRAMs) store data bits as a charge on a capacitor.
DRAMs are simple and cost effective, but require refresh circuitry to prevent losing data. The address lines are multiplexed to reduce the number of address lines.
Row address is latched when RAS is LOW
Column address is latched when CAS is LOW
Addresses
RAS
CAS
Multiplexed address lines:

## Slide 13
Summary
Dynamic RAM (DRAM)
A feature with some DRAMs is fast page mode. Fast page mode allows successive read or write operations from a series of columns address that are all on the same row.
Addresses
RAS
CAS
R/W
DOUT
Other types of DRAMs have been developed to speed access and make the processor more efficient. These include EDO DRAMs, BEDO DRAMs and SDRAMs, as described in the text.

## Slide 14
Summary
Read-Only Memory (ROM)
The ROM family is all considered non-volatile, because it retains data with power removed. It includes various members that can be either permanent memory or erasable.
ROMs are used to store data that is never (or rarely) changed such as system initialization files. ROMs are non-volatile, meaning they retain the data when power is removed, although some ROMs can be reprogrammed using specialized equipment.

## Slide 15
Summary
Read-Only Memory (ROM)
A ROM symbol is shown with typical inputs and outputs. The triangles on the outputs indicate it is a tri-stated device.
To read a value from the ROM, an address is placed on the address bus, the chip is enabled, and a short time later (called the access time), data appears on the data bus.
Address input lines
A0
A1
A2
A3
A4
A5
A6
A7
E0
E1
O0
O1
O2
O3
Data output lines
Address input lines
Data outputs
Address transition
Data output transition
ta
Chip select
Valid data on output lines
Valid address on input lines

## Slide 16
Summary
PROMs, EPROMs and EEPROMs
PROMs are programmable ROM, in which a fused link is burned open during the programming process. Once the PROM is programmed, it cannot be reversed.
An EPROM is an erasable PROM and can be erased by exposure to UV light through a window. To program it, a high voltage is applied to VPP and OE is brought LOW.
O0
O1
O2
O3
O4
O5
O6
O7
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
CE/PGM
OE
VPP
Another type of erasable PROM is the EEPROM, which can be erased and programmed with electrical pulses.

## Slide 17
Summary
Flash Memory
Flash memories are high density read/write memories that are nonvolatile. They have the ability to retain charge for years with no applied power.
Flash memory uses a MOS transistor with a floating gate as the basic storage cell. The floating gate can store charge (logic 0) when a positive voltage is applied to the control gate. With little or no charge, the cell stores a logic 1.
logic 0 is stored
logic 1 is stored
The flash memory cell can be read by applying a positive voltage to the control gate. If the cell is storing a 1, the positive voltage is sufficient to turn on the transistor; if it is storing a 0, the transistor is off.

## Slide 18
Summary
Flash Memory
Flash memories arranged in arrays with an active load. For simplicity, only one column is shown. When a specific row and column is selected during a read operation, the active load has current.
One drawback to flash memory is that once a bit has been set to 0, it can be reset to a 1 only by erasing an entire block of memory. Another limitation is that flash memory has a large but finite number of read/write cycles.

## Slide 19
Summary
Memory Expansion
Memory can be expanded in either word size or word capacity or both.
To expand word size:
Notice that the data bus size is larger, but the number of address is the same.

## Slide 20
Summary
Memory Expansion
To expand word capacity, you need to add an address line as shown in this example
Notice that the data bus size does not change.
Question
What is the purpose of the inverter?
Answer
Only one of the ICs is enabled at any time depending on the logic on the added address line.

## Slide 21
Summary
SIMMs and DIMMs
SIMMs (single in-line memory modules) and DIMMs (dual in-line memory modules) are plug-in circuit boards containing the ICs and I/O brought out on edge connectors. SIMMs have a 32-bit data path with I/O on only one side whereas DIMMs have a 64-bit data path with I/O on both sides of the board.
SIMM or DIMM
Socket on system board

## Slide 22
Summary
FIFO Memory
FIFO means first in-first out. This type of memory is basically an arrangement of shift registers. It is used in applications where two systems communicate at different rates.

## Slide 23
Summary
LIFO Memory
LIFO means last in-first out. In microprocessors, a portion of RAM is devoted to this type of memory, which is called the stack. Stacks are very useful for temporary storage of internal registers, so that the processor can be interrupted but can easily return to a given task.
A special register, called the stack pointer, keeps track of the location that data was last stored on the stack. This will be the next data to be taken from the stack when needed.
Top-of-stack
Stack pointer

## Slide 24
Summary
Magnetic Hard Drive
The magnetic hard drive is the backbone of computer mass storage and is applied to other devices such as digital video recorders. Capacities of hard drives have increased exponentially, with 1 TB (1 trillion bytes!) drives available today.
Platters are arranged in tracks (circular shapes) and sectors (pie shaped). Files are listed in a File Allocation Table, (FAT) that keeps track of file names, locations, size, and more.
Hard drive with cover removed

## Slide 25
Summary
Optical Storage
The compact disk (CD) uses a laser to burn tiny pits into the media. Surrounding the pits are flat areas called lands. The CD can be read using a low-power IR laser that detects the difference between pits and lands.
Binary data is encoded with a special method called negative non-return to zero encoding. A change from a pit to a land or a land to a pit represents a binary one, whereas no change represents a zero. A standard 120 mm CD can hold approximately 700 MB of data.

## Slide 26
Selected Key Terms
Address
Capacity
SRAM
DRAM
PROM
The location of a given storage cell or group of cells in memory.
The total number of data units (bits, nibbles, bytes, words) that a memory can store.
Static random access memory; a type of volatile read/write semiconductor memory.
Dynamic random access memory; a type of read/write memory that uses capacitors as the storage elements and is a volatile read/write memory.
Programmable read-only memory; type of semiconductor memory.

## Slide 27
Selected Key Terms
EPROM
Flash memory
FIFO
LIFO
Hard disk
Erasable programmable read-only memory; a type of semiconductor memory device that typically uses ultraviolet light to erase data.
A nonvolatile read/write random access semiconductor memory in which data are stored as charge on a floating gate of a certain type of FET.
First in-first out memory.
Last in-first out memory
A magnetic storage device; typically a stack of two or more rigid disks enclosed in a sealed housing.

## Slide 28
1. Static RAM is
a. nonvolatile read only memory
b. nonvolatile read/write memory
c. volatile read only memory
d. volatile read/write memory
Quiz

## Slide 29
2. A nonvolatile memory is one that
  a. requires a clock
  b. must be refreshed regularly
c. retains data without power applied
d. all of the above
Quiz

## Slide 30
3. The advantage of dynamic RAM over static RAM is that
a. it is much faster
b. it does not require refreshing
c. it is simpler and cheaper
d. all of the above
Quiz

## Slide 31
4. The first step in a read or write operation for a random access memory is to
a. place a valid address on the address bus
b. enable the memory
c. send or obtain the data
d. start a refresh cycle
Quiz

## Slide 32
Quiz
5. The output enable signal (OE) on a RAM is active
  a. only during a write operation
  b. only during a read operation
c. both of the above
d. none of the above

## Slide 33
Quiz
6. When data is read from RAM, the memory location is
  a. cleared after the read operation
  b. set to all 1’s after the read operation
c. unchanged
d. destroyed

## Slide 34
7. An EPROM has a window to allow UV light to enter under certain conditions. The purpose of this is to
a. refresh the data
b. read the data
c. program the IC
d. erase the data
Quiz

## Slide 35
8. The small triangles on the logic diagram indicate that these outputs are
a. not used
b. tri-stated
c. inverted
d. grounded
Quiz
Address input lines
A0
A1
A2
A3
A4
A5
A6
A7
E0
E1
O0
O1
O2
O3
Data output lines

## Slide 36
9. Using two ICs as shown will expand
a. the word size
b. the number of words available
c. both of the above
d. none of the above
Quiz

## Slide 37
10. On a hard drive. information about file names, locations, and file size are kept in a special location called the
a. file location list
b. file allocation table
c. disk directory
d. stack
Quiz

## Slide 38
Answers:
1. d
2. c
3. c
4. a
5. b
6. c
7. d
8. b
9. a
10. b
Quiz