## Slide 1: Digital Logic & Systems Latches and Flip-Flops
Wenye Li, Ph.D
The Chinese University of Hong Kong

## Slide 2
A latch is a temporary storage device that has two stable states (bistable). It is a basic form of memory.
Summary
Latches
The S-R (Set-Reset) latch is the most basic type. It can be constructed from NOR gates or NAND gates. With NOR gates, the latch responds to active-HIGH inputs; with NAND gates, it responds to active-LOW inputs.
NOR Active-HIGH Latch NAND Active-LOW Latch
R
S
Q
Q
Q
S
R
Q

## Slide 3
The active-HIGH S-R latch is in a stable (latched) condition when both inputs are LOW.
Summary
Latches
R
S
Q
Q
Assume the latch is initially RESET (Q = 0) and the inputs are at their inactive level (0). To SET the latch (Q = 1), a momentary HIGH signal is applied to the S input while the R remains LOW.
0
1
0
R
S
Q
Q
1
0
0
To RESET the latch (Q = 0), a momentary HIGH signal is applied to the R input while the S remains LOW.
0
0
1
0
1
0
Latch initially RESET
Latch initially SET

## Slide 4
S
R
The active-LOW S-R latch is in a stable (latched) condition when both inputs are HIGH.
Summary
Latches
Q
Q
1
1
0
1
0
1
Latch initially RESET
Q
Q
1
1
0
1
0
1
Latch initially SET
S
R
Assume the latch is initially RESET (Q = 0) and the inputs are at their inactive level (1). To SET the latch (Q = 1), a momentary LOW signal is applied to the S input while the R remains HIGH.
To RESET the latch a momentary LOW is applied to the R input while S is HIGH.
Never apply an active set and reset at the same time (invalid).

## Slide 5
The active-LOW S-R latch is available as the 74LS279A IC.
Summary
Latches
1Q
2Q
3Q
4Q
74LS279A
It features four internal latches with two having two S inputs. To SET any of the latches, the S line is pulsed low. It is available in several packages.
Position 1 to 2
Position 2 to 1
S
R
Q
VCC
S-R latches are frequently used for switch debounce circuits as shown:
S
R

## Slide 6
Summary
Latches

## Slide 7
Summary
Latches

## Slide 8
A gated latch is a variation on the basic latch.
Summary
Latches
The gated latch has an additional input, called enable (EN) that must be HIGH in order for the latch to respond to the S and R inputs.
R
S
Q
Q
EN
Show the Q output with relation to the input signals. Assume Q starts LOW.
Example
Solution
Keep in mind that S and R are only active when EN is HIGH.
S
R
EN
Q

## Slide 9
Summary
Latches
The D latch is an variation of the S-R latch but combines the S and R inputs into a single D input as shown:
A simple rule for the D latch is:
Q follows D when the Enable is active.
D
EN
Q
Q
Q
Q
D
EN

## Slide 10
Summary
Latches
The truth table for the D latch summarizes its operation. If EN is LOW, then there is no change in the output and it is latched.

## Slide 11
Summary
Latches
Determine the Q output for the D latch, given the inputs shown.
Notice that the Enable is not active during these times, so the output is latched.
Q
Q
D
EN
Example

## Slide 12
Summary
D Flip-flop
A flip-flop differs from a latch in the manner it changes states. A flip-flop is a clocked device, in which only the clock edge determines when a new bit is entered.
The active edge can be positive or negative.
Dynamic input indicator

## Slide 13
Summary
D Flip-flop
The truth table for a positive-edge triggered D flip-flop shows an up arrow to remind you that it is sensitive to its D input only on the rising edge of the clock; otherwise it is latched. The truth table for a negative-edge triggered D flip-flop is identical except for the direction of the arrow.
(a) Positive-edge triggered (b) Negative-edge triggered

## Slide 14
Summary
D Flip-flop

## Slide 15
Summary
D Flip-flop

## Slide 16
Summary
D Flip-flop

## Slide 17
Summary
J-K Flip-flop
The J-K flip-flop is more versatile than the D flip flop. In addition to the clock input, it has two inputs, labeled J and K. When both J and K = 1, the output changes states (toggles) on the active clock edge (in this case, the rising edge).

## Slide 18
Summary
J-K Flip-flop
Determine the Q output for the J-K flip-flop, given the inputs shown.
Example
CLK
Q
K
J
CLK
K
J
Q
Q
Notice that the outputs change on the leading edge of the clock.
Solution
Set
Toggle
Set
Latch

## Slide 19
Summary
J-K Flip-flop

## Slide 20
Summary
Flip-flops
CLK
D
CLK
Q
Q
A D-flip-flop does not have a toggle mode like the J-K flip-flop, but you can hardwire a toggle mode by connecting Q back to D as shown. This is useful in some counters as you will see in later chapters.
For example, if Q is LOW, Q is HIGH and the flip-flop will toggle on the next clock edge. Because the flip-flop only changes on the active edge, the output will only change once for each clock pulse.
D flip-flop hardwired for a toggle mode

## Slide 21
Summary
Flip-flops
Synchronous inputs are transferred in the triggering edge of the clock (for example the D or J-K inputs). Most flip-flops have other inputs that are asynchronous, meaning they affect the output independent of the clock.
Two such inputs are normally labeled preset (PRE) and clear (CLR). These inputs are usually active LOW. A J-K flip flop with active LOW preset and CLR is shown.
CLK
K
J
Q
Q
PRE
CLR

## Slide 22
Summary
Flip-flops
Flip-flops
Determine the Q output for the J-K flip-flop, given the inputs shown.
Example
CLK
K
J
Q
Q
PRE
CLR
Solution
Set
Toggle
Reset
Toggle
Set
Set
Reset
Latch
CLK
K
J
Q
PRE
CLR

## Slide 23
Propagation delay time is specified for the rising and falling outputs. It is measured between the 50% level of the clock to the 50% level of the output transition.
Summary
Flip-flop Characteristics
50% point on triggering edge
50% point
50% point on LOW-to-HIGH transition of Q
tPLH
tPHL
CLK
CLK
Q
Q
50% point on HIGH-to- LOW transition of Q
The typical propagation delay time for the 74AHC family (CMOS) is 4 ns. Even faster logic is available for specialized applications.

## Slide 24
Another propagation delay time specification is the time required for an asynchronous input to cause a change in the output. Again it is measured from the 50% levels. The 74AHC family has specified delay times under 5 ns.
Summary
Flip-flop Characteristics
50% point
tPLH
tPHL
Q
50% point
50% point
50% point
Q
PRE
CLR

## Slide 25
Set-up time and hold time are times required before and after the clock transition that data must be present to be reliably clocked into the flip-flop.
Summary
Flip-flop Characteristics
Setup time is the minimum time for the data to be present before the clock.
Hold time is the minimum time for the data to remain after the clock.
CLK
D
CLK
D
Set-up time, ts
Hold time, tH

## Slide 26
Other specifications include maximum clock frequency, minimum pulse widths for various inputs, and power dissipation. The power dissipation is the product of the supply voltage and the average current required.
Summary
Flip-flop Characteristics
A useful comparison between logic families is the speed-power product which uses two of the specifications discussed: the average propagation delay and the average power dissipation. The unit is energy.
Example: the average propagation delay for 74AHC74A is 4.6 ns. The quiescent power dissipated is 1.1 mW. Therefore, the speed-power product is
5 pJ

## Slide 27
Summary
Flip-flop Applications
Principal flip-flop applications are for temporary data storage, as frequency dividers, and in counters (which are covered in detail in later chapters).
Typically, for data storage applications, a group of flip-flops are connected to parallel data lines and clocked together. Data is stored until the next clock pulse.
Parallel data input lines
Clock
Clear
Output lines
Q0
Q1
Q2
Q3

## Slide 28
Summary
Flip-flop Applications
For frequency division, it is simple to use a flip-flop in the toggle mode or to chain a series of toggle flip flops to continue to divide by two.
One flip-flop will divide fin by 2, two flip-flops will divide fin by 4 (and so on). A side benefit of frequency division is that the output has an exact 50% duty cycle.
HIGH
HIGH
CLK
K
J
QA
CLK
K
J
fin
QB
fout
Waveforms:
fin
fout

## Slide 29
Selected Key Terms
Latch
Bistable
Clock
D flip-flop
J-K flip-flop
A bistable digital circuit used for storing a bit.
Having two stable states. Latches and flip-flops are bistable multivibrators.
A triggering input of a flip-flop.
A type of bistable multivibrator in which the output assumes the state of the D input on the triggering edge of a clock pulse.
A type of flip-flop that can operate in the SET, RESET, no-change, and toggle modes.

## Slide 30
Selected Key Terms
Propagation delay time
Set-up time
Hold time
The interval of time required after an input signal has been applied for the resulting output signal to change.
The time interval required for the input levels to be on a digital circuit.
The time interval required for the input levels to remain steady to a flip-flop after the triggering edge in order to reliably activate the device.

## Slide 31
1. The output of a D latch will not change if
a. the output is LOW
b. Enable is not active
c. D is LOW
d. all of the above
Quiz

## Slide 32
2. The D flip-flop shown will
a. set on the next clock pulse
b. reset on the next clock pulse
c. latch on the next clock pulse
d. toggle on the next clock pulse
Quiz
CLK
D
CLK
Q
Q

## Slide 33
3. For the J-K flip-flop shown, the number of inputs that are asynchronous is
a. 1
b. 2
c. 3
d. 4
Quiz
CLK
K
J
Q
Q
PRE
CLR

## Slide 34
4. Assume the output is initially HIGH on a leading edge triggered J-K flip flop. For the inputs shown, the output will go from HIGH to LOW on which clock pulse?
a. 1
b. 2
c. 3
d. 4
Quiz
CLK
K
J
1 2 3 4

## Slide 35
5. The time interval illustrated is called
a. tPHL
b. tPLH
c. set-up time
d. hold time
Quiz
50% point on triggering edge
50% point on LOW-to-HIGH transition of Q
CLK
Q
?

## Slide 36
Quiz
CLK
D
?
6. The time interval illustrated is called
a. tPHL
b. tPLH
c. set-up time
d. hold time

## Slide 37
7. The application illustrated is a
a. astable multivibrator
b. data storage device
c. frequency multiplier
d. frequency divider
Quiz
HIGH
HIGH
CLK
K
J
QA
CLK
K
J
fin
QB
fout

## Slide 38
Answers:
1. b
2. d
3. b
4. c
5. b
6. d
7. d
Quiz